MH320 Portable Hardness Tester

Advantages

Large screen(128×64 dot matrix LCD), showing all functions and parameters.

Test at any angle, even upside down.

Wide measuring range. It can measure the hardness of all metallic materials. Direct display of hardness scales HRB, HRC, HV, HB, HS, HL and three types of strength values immediately.

Seven impact devices are available for special application. Automatically identify the type of impact devices.

Large capacity memory could store 500 groups (Relative to average times32～1 ) information including single measured value, mean value, testing data, impact direction, impact times, material and hardness scale etc.

Upper and lower limit can be preset. It will alarm automatically when the result value exceeding the limit.

Battery information indicates the rest capacity of the battery and the charge status.

User calibration function.

USB port with the PC humanity multi-functions data proceeding software.

Original imported high speed thermal printer support the immediate printing function. It can save data permanently.

NI-MH rechargeable battery as the power source. Charge circuit integrated inside the instrument. Continuous working period of no less than 150 hours (EL off and no printing).

Auto power off to save energy.

Excellent after-sale service system for high quality products---two years’ guarantee and all life maintenance. Easy to buy and comfortable to use.

Main Application

Die cavity of molds

Bearings and other parts

Failure analysis of pressure vessel, steam generator and other equipment

Heavy work piece

The installed machinery and permanently assembled parts

Testing surface of a small hollow space

Material identification in the warehouse of metallic materials

Rapid testing in large range and multi-measuring areas for large-scale work piece

Technical Specifications

Measuring range：HLD（170～960）HLD

Measuring direction：360°

Hardness Scale：HL、HB、HRB、HRC、HRA、HV、HS

Display：dot matrix LCD，128×64 dots

Data memory： 500 groups max.（relative to impact times 32～1）

Printing paper: width is （57.5±0.5）mm, diameter is 30mm

Battery pack: 6V NI-MH

Battery charger: 9V/500mA

Continuous working period：about 150 hours（With backlight off, no printing）

Communication interface：USB1.1

Outline dimensions：212mm×80mm×32mm

### Configuration

|  | No. | Item | Quantity | Remarks |
| --- | --- | --- | --- | --- |
| Standard Configuration | 1 | Main Unit | 1 |  |
|  | 2 | D type impact device | 1 | With cable |
|  | 3 | Standard test block | 1 |  |
|  | 4 | Cleaning brush (I) | 1 |  |
|  | 5 | Small support ring | 1 |  |
|  | 6 | Battery Charger | 1 | 9V 500mA |
|  | 7 | Paper for printing | 1 |  |
|  | 8 | Manual | 1 |  |
|  | 9 | Instrument case | 1 |  |
|  | 10 | DataPro software | 1 |  |
|  | 11 | Communication cable | 1 |  |
| Optional Configuration | 12 | Cleaning brush (II) | 1 | For use with G type impact device |
|  | 13 | Other type of impact devices and support rings |  | Refer to Table 3 and Table 4 in the appendix. |
|  | 14 |  |  |  |
|  | 15 |  |  |  |
|  | 16 |  |  |  |

www.cnrinch.com   cnrinch@yahoo.com.cn